## Slide 1
Q-Learning Driven Spectrum Prediction for
Energy-Efficient RF-Powered D2D Communications
Dr. Avik Banerjee
Assistant Professor
ECE department
RV College of Engineering, Bengaluru, India
Slide 1

## Slide 2
Q-Learning Driven Spectrum Prediction for
Energy-Efficient RF-Powered D2D Communications
Dr. Avik Banerjee
Assistant Professor
ECE department
RV College of Engineering, Bengaluru, India
Slide 2

## Slide 3
Introduction
Literature Review
System Model
Problem Formulation
MDP and Q learning
Simulation Results
Conclusion with scope of Future Works
References
Slide 3

## Slide 4
Introduction to Cognitive Radio
Slide 4

## Slide 5
 | Introduction to Cognitive radio |  |  |  |  |  | 
Exchange short packets (few information bytes), efficient frequency access or sharing, ultra-high reliability (low outage) and low latency (through efficient routing) [1-3].
Challenges:
Energy Crisis, Spectrum Scarcity, Data Transmission, Security
Solution: Cognitive Radio (CR) [1,4,5]: Cooperative Communication, Spectrum Sensing (SS), Spectrum Prediction (SP), Energy Harvesting (EH) [4], Markov Decision process (POMDP) boosting D2D data transmission [8].
Slide 5

## Slide 6
 | Literature Review |  | Spectrum Prediction |  |  |  | 
Of late Hidden Markov Model (HMM), long short term memory (LSTM) and convolution neural network (CNN) have been used to build up SP model. ML techniques on SS and
SP are also been reported [5]–[7], [9].
In [5], PU transmission behavior is predicted using an support vector machine (SVM) model, eliminating explicit spectrum sensing, while a deep Q network (DQN)-based routing strategy is used to jointly improve energy efficiency (EE) and spectral efficiency (SE).
A DRL-based cooperative spectrum sensing (CSS) framework is presented in [11], where deep learning (DL) analyzes the spectrum environment and Reinforcement learning (RL) determines PU transmit decisions.
A long short term memory (LSTM)-based cooperative spectrum prediction (SP) scheme is introduced in [12] for energy-constrained CRNs, employing parallel fusion to mitigate individual prediction errors.
By modeling spectrum samples as time-series data, [13] demonstrates that LSTM networks outperform multi layer perceptron (MLP) and regression models in SP accuracy.
Slide 6

## Slide 7
 | System Model |  | Problem Formulation |  |  |  | 
Fig. 1. System model (a) proposed and (b) from [14].
Data rate
PU interference
Power Causality
D2D-based IoT system is considered as the SU network, where the device transmitter performs spectrum prediction using received PU signals to enable opportunistic spectrum access.
The system model in [14] is used for comparison to highlight operational differences, assuming a one-way DT–DR link with bidirectional communication supported via time or frequency division.
The work aims to maximize D2D EE while meeting its target data rate, PU interference protection and meeting power of transmission required to transmit device from the harvested energy. Mathematically, the problem can be written as
Problem Formulation
[14] S. P. Maity, K. Sinha, B. P. Sinha and R. Kumari,, “Reinforcement learning for spectrum prediction and EE maximization in D2D communication,” Proc. IEEE International Conference on Signal Processing and Communication, 11-15 July, 2022, IISC Bangalore, India.
Slide 7

## Slide 8
 | PU spectrum usage and predicted pattern |  |  |  |  |  | 
Fig. 2. PU spectrum usage pattern and predicted pattern.
Slide 8

## Slide 9
 | MDP Problem Formulation |  |  |  |  |  | 
The main objective is to determine the optimal value of device transmit power PD that maximizes the system EE by accurately predicting the PU state at each time slot while satisfying the above constraints.
A Markov chain model is employed to characterize the PU activity, following the Markov property with state–transition probabilities p00, p01, p11, and p10, as shown in Fig. 3.
Here, state 0 denotes that the channel is currently idle (i.e., not accessed by the PU), whereas state 1 denotes that the channel is occupied by the PU.
Fig. 3 Markov Channel Model of PU
Slide 9

## Slide 10
 | State-Action Reward |  |  |  |  |  | 
Correct prediction leads to state-action reward (r) while wrong prediction due to state-action is negatively rewarded i.e. a penalty is assigned in cumulative reward function Reward (r) and Penalty (p) are defined as follows
At time instant t, with prediction of PU spectrum state, SU updates the Q table with weight ‘w’ as follows:
where, learning and discount factors are denoted by and respectively.
Slide 10

## Slide 11
 | Pseudo-code |  |  |  |  |  | 
Eq. (9)
Eq. (10)
Slide 11

## Slide 12
 | Simulation Results |  | Result 1 |  |  |  | 
Simulation Parameter:
Fig. 4. SP accuracy: p1 and p4 vs number of epochs
The graphical plot of p1 and p4 with the number of epochs are shown in Fig. 4. Both p1 and p4 increase with the increase in the number of epoch indicating the improved learning of the system leading to high accuracy on SP. High values of p1 and p4 indicate a higher prediction accuracy for identifying PU spectrum holes and correctly detecting PU transmission, respectively.
Slide 12

## Slide 13
 | Simulation Results 2 and 3 |  |  |  |  |  | 
Fig. 5. SP accuracy: p2 and p3 vs number of epochs
Fig. 6. Normalized EE vs number of epochs
Fig. 5 shows that the proposed RL-based spectrum prediction reduces p2 and p3 with increasing training epochs, resulting in lower spectrum loss, improved protection of the primary user, and superior ROC performance compared to existing SS/SP methods.
Fig. 6 illustrates that the normalized energy efficiency increases with the number of training epochs and higher D2D data-rate constraints, as reduced prediction errors allow more transmit power for D2D communication, thereby enhancing data transmission performance.
Slide 13

## Slide 14
 | Simulation Results 3 and 4 |  |  |  |  |  | 
Fig. 7 shows that the residual energy increases with the number of training epochs, as improved PU detection keeps the energy harvester active for longer durations, resulting in higher harvested and stored energy after D2D transmission.
Fig. 8 illustrates that residual energy increases with both PU transmit power and probability p4. Fig. 8 also shows performance comparison in residual energy over [4] at Pp = 0.8 W and Pp = 0.6 W. About 35% and 50% increase are seen on the values of residual energies for the proposed method over [4].
Fig. 7. Residual energy vs number of epochs
Fig. 8. Residual energy vs PU spectrum detection probability
[4] S. Ghose, A. Kundu, D. Mishra, S. P. Maity, A. Al-Nahari, R. J¨antti, “Energy Efficient RIS-Assisted Wireless Powered D2D Communications in Cognitive Radio Networks,” IEEE Trans. on Green Commun. & Networking, vol. 9, No. 3. pp.1254-1267, 2025.
Slide 14

## Slide 15
 | Conclusions and Future Works |  |  |  |  |  | 
A reinforcement learning (Q-learning) based spectrum prediction framework is proposed to identify spectrum holes and PU transmit states in a CRN.
The proposed method maximizes energy efficiency under RF energy harvesting causality, PU interference protection, and D2D data-rate constraints with reduced training complexity.
Simulation results show 25% and 35% improvement in energy efficiency compared to [14] and [4], respectively.
PU protection is enhanced with 25% reduction in data collision over [8], along with 35% improvement in residual energy compared to [4].
Future Work:
Extension of the proposed SP framework to cooperative spectrum sensing using actor–critic based reinforcement learning.
Multi-channel PU prediction to support hybrid interweave, underlay, and overlay bidirectional D2D communications.
Investigation of non-linear energy harvesting models for more realistic system performance analysis.
Slide 15

## Slide 16
 | References |  |  |  |  |  | 
[1] Y. Li, F. Zhou, L. Yuan, Q. Wu, and N. Al-Dhahir, “Cognitive semantic communication: A new communication paradigm for 6G,” IEEE Commun. Magazine, pp.1-8, 2025.
[2] X. Liu, and N. Ansari, “Green relay assisted D2D communications with dual batteries in heterogeneous cellular networks for IoT,” IEEE Things Journal, vol. 4, no.5, pp.1707-1715, 2017.
[3] N. Du, C. Zhou, H. Shen, C. Chakraborty, J. Yang, and K. Yu, “A novel power allocation algorithm for minimizing energy consumption in D2D communication systems,” IEEE Systems Journal, vol. 17, no. 3, pp. 4969–4977, 2023.
[4] S. Ghose, A. Kundu, D. Mishra, S. P. Maity, A. Al-Nahari, R. J¨antti, “Energy Efficient RIS-Assisted Wireless Powered D2D Communications in Cognitive Radio Networks,” IEEE Trans. on Green Commun. & Networking, vol. 9, No. 3. pp.1254-1267, 2025.
[5] A. Paul, and S. P. Maity, “Machine learning for spectrum information and routing in multi-hop green cognitive radio networks,” IEEE Trans.on Green Commn. & Network, vol. 6, no.23 pp.825-835, 2022.
[6] N. El-haryqy, Z. Madini, and Y. Zouine, “A review of deep learning techniques for enhancing spectrum sensing and prediction in cognitive radio systems: approaches, datasets, and challenges,” Int. Journ. Comput. Appl., vol. 46, no.12 pp.1104-1128, 2024.
[7] L. Feng, Y. Gao, Z. Xu, L. Yu, and Y. Cheng, “Deep learning-based intelligent spectrum sensing and prediction: A survey,” IEEE Access, vol. 10, no.12 pp.13078-13096, 2022.
[8] R. Sarikhani and F. Keynia, “Cooperative spectrum sensing meets machine learning:deep reinforcement learning approach,” IEEE Commn. Lett., vol. 24, no.7 pp.1459-1462, 2020.
Slide 16

## Slide 17
 | References |  |  |  |  |  | 
[9] A. Paul, S. Das and S. P. Maity, “Spectrum Prediction: Boosting D2D communications in CRNs using POMDP,” Physical Communications, vol. 71, pp.102704, 2025.
[10] Y. Li, J. Wu, Y. Lou, X. Xu, and J. Bao, “Enhanced support vector machine for cooperative spectrum sensing against byzantine attack in cognitive wireless sensor networks,” IEEE Sens. J, vol. 24, No. 23.
pp.39835-39844, 2024.
[11] S. Q. Jalil, M. H. Rehmani and S. Chalup, “Cognitive radio spectrum sensing and prediction using deep reinforcement learning,” Proc. Inter. Joint Conf. on Neural Networks, 18-22 July, 2021, Shenzhen, China.
[12] P. Chauhan, S. K. Deka, B. C. Chatterjee and N. Sarma, “Cooperative spectrum prediction-driven sensing performance for energy constrained cognitive radio networks,” IEEE Access, vol.9, pp.26107-26118, 2021.
[13] L. Yu, J. Chen, G. Ding, J. Yang and H. Sun, “Spectrum prediction based on Taguchi method in deep learning with long short-term memory,” IEEE Access, vol.6, pp.45923-45933, 2018.
[14] S. P. Maity, K. Sinha, B. P. Sinha and R. Kumari,, “Reinforcement learning for spectrum prediction and EE maximization in D2D communication,” Proc. IEEE International Conference on Signal Processing
and Communication, 11-15 July, 2022, IISC Bangalore, India.
[15] H. Ding, X. Li, Y. Ma, and Y. Fang, “Energy-efficient channel switching in cognitive radio networks: A reinforcement learning approach,” IEEE Trans. Veh. Technol., vol.69, no. 10,pp.12359-12362, 2020.
Slide 17

## Slide 18
 | Thank You |  |  |  |  |  | 
Slide 18